## Slide 1
The air pollution exposome
Dimosthenis A. Sarigiannis1,2,3,4
1 Aristotle University of Thessaloniki, Department of Chemical Engineering, Environmental Engineering Laboratory, University Campus, Thessaloniki 54124, Greece
2 HERACLES Research Center on the Exposome and Health, Center for Interdisciplinary Research and Innovation, Balkan Center, Bldg. B, 10th km Thessaloniki-Thermi Road, 57001, Greece
3 University School for Advanced Study (IUSS), Science, Technology and Society Department, Environmental Health Engineering, Piazza della Vittoria 15, Pavia 27100, Italy
4 EnvE.X, Thessaloniki, K. Palama 11, Thessaloniki, 55133, Greece
http://www.enve-lab.eu/

## Slide 2
Training loop
Chart: Index
| Nasopharyngeal | Tracheobronchial | Pulmonary bronchioles | Nasopharyngeal | Tracheobronchial | Pulmonary bronchioles | Traffic | Urban background
Q1 | 3.0222 | 0.74532 | 1.6002 | 1.0921 | 0.27991 | 0.53211
Q2-Q1 | 10.6687 | 2.4834 | 5.3642 | 3.1774 | 0.87176 | 1.254
25%-75% | 6.0229 | 4.721 | 10.8547 | 2.658 | 2.0829 | 4.4205
Mean | 13.8017 | 3.7589 | 7.5216 | 4.6111 | 1.2438 | 1.929
AQ models and data fusion
HRT deposition
+
INTEGRA platform
Sensors data
Source apportionment
ABM
Meteo-data
AQ
monitoring
Remote sensing
ANN model
AQ models
Chemical analysis
Industry / energy
Waste management
Transportation
Agriculture
SES
Health impact
Carbon footprint models
Chart: Index
| Nasopharyngeal | Tracheobronchial | Pulmonary bronchioles | Nasopharyngeal | Tracheobronchial | Pulmonary bronchioles | Traffic | Urban background
Q1 | 3.0222 | 0.74532 | 1.6002 | 1.0921 | 0.27991 | 0.53211
Q2-Q1 | 10.6687 | 2.4834 | 5.3642 | 3.1774 | 0.87176 | 1.254
25%-75% | 6.0229 | 4.721 | 10.8547 | 2.658 | 2.0829 | 4.4205
Mean | 13.8017 | 3.7589 | 7.5216 | 4.6111 | 1.2438 | 1.929
Monetary impact
Chart: Index
| Nasopharyngeal | Tracheobronchial | Pulmonary bronchioles | Nasopharyngeal | Tracheobronchial | Pulmonary bronchioles | Traffic | Urban background
Q1 | 3.0222 | 0.74532 | 1.6002 | 1.0921 | 0.27991 | 0.53211
Q2-Q1 | 10.6687 | 2.4834 | 5.3642 | 3.1774 | 0.87176 | 1.254
25%-75% | 6.0229 | 4.721 | 10.8547 | 2.658 | 2.0829 | 4.4205
Mean | 13.8017 | 3.7589 | 7.5216 | 4.6111 | 1.2438 | 1.929
Climate forcing
Health effects
Climate forcing models
Exposure modeling
GHG monitoring
ICARUS methodology
Integrated climate change and air pollution management
Notes: Air pollution monitoring and assessment will be based on:
Ground-based measurements based on smart sensors that transfer information through IoT
Ground-based measurements from the existing AQ stations network of the municipality of Thessaloniki
Different atmospheric modelling techniques
Satellite-derived information
Moreover: we’ll have campaigns with new and smart sensor technologies to estimate individual exposure.
with the help of machine learning techniques we’ll have a data fusion of all theses sources of information to reach air pollution assessment at the highest spatial resolution.
We will also use improved source apportionment methods so that we have a relationship between emission and concentration variation
Moreover, we will make use of ABM (separate presentation) to simulate the interactions of several population groups in response to the policies considered in the project. In this scope, sociodemographic factors will be explicitly taken into account.
We will deploy carbon footprint models based on all simulated activities and we will establish country-specific Concentration-Response Functions (CRFs) for an improved heath impact assessment on personal and community level.

## Slide 3
Exposure modelling
Systems Effects / Individual exposome
Community
Effects / Cohorts
GI tract – portal vein
Liver
Heart
Brain
Muscles
Skin
Kidneys
Adipose
Bones
Breast
Uterus - gonads
Lungs
GI tract – portal vein
Liver
Heart
Brain
Muscles
Skin
Kidneys
Adipose
Bones
Breast
Uterus - gonads
Lungs
metabolite
formation
Arterial blood
Venous blood
Arterial blood
Venous blood
Cellular/tissue effects
Molecular initiating events
Transcriptomics
Ubiquitous personal sensors
Environmental sensors
Environmental modeling / data management
Remote sensing
Environmental analysis
Human biosampling
Agent based modelling
Metabolomics
Fluxomics
(dynamic flux balance analysis)
Pathway
analysis
Bioinformatics / systems biology
EWAS
Epigenetics
Genomics
The air pollution exposome
Environmental data
Biological data
Clinical data

## Slide 4
Exposure biology workflow
Rendering high dimension biology operational
Untargeted metabolite profiling
LC-MS/MS, MS/MS-ToF, NMR
Whole genome mRNA expression
mRNA Microarrays
Molecular pathways
Metabolic pathways
PoT hypothesis
Targeted proteomics
Targeted metabolomics
Targeted DNA
Methylation analysis
Phenotypic/endotypic
anchoring
Targeted (bio)chemical analysis
Functional assays

## Slide 5
What are the real life PM/NP emission characteristics of older and newer vehicles?
How are these emissions translated into human exposure and health effects?
Rationale

## Slide 6
Methodology
Environmental and exposure assessment
Laser Particle Sizer analyzer
Scanning electron
microscopy
HR-ICP-MS
Real life emissions
18 car with low mileage (P+D)
17 cars with high mileage (P+D)
Inhalation exposure
HRT model
Diffusion Sedimentation Impaction

## Slide 7
Results
PM size distribution and active surface –
newer vs older vehicles
Newer diesel vehicles emit smaller particles, with a higher active surface and toxic content

## Slide 8: Biological effects of air pollution
The complexity of biological responses following exposure to nanoparticles underlines the need for the development of dedicated and comprehensive methodologies to approach the potential health effects of nanomaterials.
In vitro
In vivo (animal model)
In vivo (human volunteers)
Lipidomics
Transcriptomics
Immunologic response
Pathway Architect
GeneSpring Platform
Mechanism identification

## Slide 9
Comparison between cell lines: Ha-CaT and A549 (48h)
Ha-CaT
A549
common genes
Inflammation mediated by chemokine and
cytokine signaling pathway
SW
MW
NH2
COOH
Inflammation Pathway Genes
Total Genes

## Slide 10: Gene expression modulation in lung of mice 1d after i. tr. exposure to nanotubes (1mg/Kg b.w.)

## Slide 11: Lung, mice 24h, Oxidative stress response pathway
MWCNT
-NH2
= MW
= NH2
= common
MWCNT
-COOH
= MW
= COOH
= common

## Slide 12: In vivo (mice) Lung, 24h, Inflammation mediated by chemokine and cytokine signaling pathway
MWCNT
-NH2
= MW
= NH2
= common
= MW
= COOH
= common
MWCNT
-COOH

## Slide 13: In vivo (mice) Modulation of chemokines gene expression in lung of mice 1d after i. tr. exposure to nanotubes (1mg/kg_bw)
Value of gene expression by Quantitative RT-PCR and microarrays.
RT-PCR: significantly modulated over 96 tested.
Fold Change (FC) > 3
Chart: Genes expression modulation
| SWCNT | MWCNT | MW-NH2 | MW-COOH
Ccl19 | 1.4 | 1.7 | 1.45 | 3.75
Ccl2 | 4.4 | 1.35 | 3.4 | 29.5
Cxcl10 | 1.4 | 1.05 | 1.9 | 18.3
Ccl22 | 0.8 | 0.55 | 1.75 | 27.9
3 fold change threshold | 3 | 3 | 3 | 3

## Slide 14: In vitro (A549) and in vivo (mice lungs) Inflammation mediated by chemokine and cytokine signaling pathway
A549
= MW
= COOH
= common
Mice Lungs

## Slide 15: In vivo - Human volunteers Lipidomics in the blood of healthy volunteers after exposure to SWCNTs and MWCNTs of different functionalization
Chart: Lipid peroxidation products (abs. units)
| Pre-exposure | SWCNT | MWCNT | MW-NH2 | MW-COOH
LHP | 2.2 | 3.89 | 4.1 | 5.6 | 6.3
CCIDB - Neutral | 3.69 | 4.23 | 4.7 | 5.3 | 5.6
DC - Neutral | 1.94 | 2.55 | 2.8 | 3.4 | 4.3
KD+CT - Neutral | 0.52 | 0.7 | 0.76 | 0.81 | 0.94
CCIDB - Phospholipids | 2.1 | 1.47 | 1.53 | 1.8 | 2.5
DC - Phospholipids | 1.02 | 0.68 | 0.71 | 0.8 | 1.23
KD+CT - Phospholipids | 0.47 | 0.32 | 0.52 | 0.63 | 0.74
Notes: Biochemical analyses were used to assess the levels of primary products of lipid peroxidation (LPO) – lipid hydroperoxides (LHP) and the intermediate products of LPO – diene conjugates (DC), ketodienes (KD), conjugated trienes (CT), compounds containing isolated double bonds (CCIDB).
Oxidative disorders were manifested in the form of increase in the content of the primary products of lipid peroxidation (LPO) and redistribution of the intermediate products (CCIDB, DC, KD+CT) in neutral lipids and phospholipids of blood cell membranes.
The load test by the MWCNTs with more complex functionalization caused a significant increase in LHP levels on the whole blood as compared to the SWCNTs (1.5 times, р 0.05) and 2.6 times as compared to the untreated blood.
The fatty acids (FA) of neutral lipids and the free FA of plasma are more susceptible to peroxidation by MWCNTs with more complex functionalization than the FA of membrane phospholipids. This was evidenced by the increased levels of KD and CT (35%, р0.01 and 28%, р 0.05) and the stable levels of CCIDB and DC. This may be due to reoxidation reactions of low polar neutral lipids on the surface of non-polar MWCNTs that are highly able to adsorb non-polar substances

## Slide 16: In vivo - Human volunteers Immunological parameters in the blood of healthy volunteers after exposure to SWCNTs and MWCNTs of different functionalization
Chart: immunological parameters (%)
| Pre-exposure | SWCNT | MWCNT | MW-NH2 | MW-COOH
CD3+CD95+ | 9.2 | 14.4 | 14.9 | 15.2 | 16.3
CD3+CD25+ | 7.4 | 12.3 | 13.1 | 13.3 | 14.6
CD3+CD126+ | 1.2 | 1.8 | 1.95 | 2.1 | 2.8
MMPL | 1.3 | 3.1 | 3.4 | 4.4 | 6.2
MMP CD3+ | 3.1 | 4.6 | 4.9 | 5.7 | 8.1
#REF! | 1
#REF! | 1
Notes: Exposure to MWCNTs caused an increase in the percentage of immune cells with reduced mitochondrial membrane potential. The number of mature T lymphocytes with reduced potential underwent a more than three-fold increase.
At the same time, upregulation of the pre-apoptotic CD95 marker on CD3+ cells was observed. MWCNTs activated the early phase of T-cell response and caused an increase in the percentage of the functionally active T lymphocytes expressing interleukin-6 (IL-6 receptor (CD3+CD126+).
The damaging effect of MWCNTs of different degree of functionalization was manifested in the significant increase in the percentage of lymphocytes and CD3+ cells with reduced mitochondrial membrane potential (MMPL and MMP СD3+ respectively).
upregulation of the pre-apoptotic CD95, CD25 and CD126 markers on CD3+ cells was observed

## Slide 17: Up-regulation of anti-apoptotic pathway in the presence of carbon nanoparticles
Notes: NFκB regulates the expression of many genes involved in inflammation, including the pre-inflammatory cytokines IL-1b, TNF-α and IL-6
This may cause a perturbation of the IL-6 pathway that aims to regulate the inflammatory processes and compensate apoptotic changes
IL-6 is an early and very important mediator in the development of inflammation. Elevated levels of IL-6 contribute to the maintenance of oxidative stress
The increased mitochondrial production of reactive oxygen species are triggered by overproduction of the mitochondrial reduced form of nicotinamide-adenine dinucleotide (NADH). However both NADH-driven mitochondrial MPT and up-regulation of the expression of CD95-Fas ligand (FasL)-mediated apoptosis, involving in reactive oxygen species production, operates apoptosis
In inflammation, TNF-α induces mitochondrial permeability transition pore (MPTP) opening, mitochondrial membrane potential loss, and increased cell apoptosis.
From the overall results of our multi-level analysis, it seems that the key biological process resulting from exposure with CNTs is NFκB activation.
Based on the combined biochemical and transcriptomic responses in our study, the synergistic effect of systemic inflammation mediated in exposure barriers (skin and lung epithelium) and local inflammation mediated in blood cells, forms a plausible hypothesis for immunological in vivo responses upon exposure to CNTs.

## Slide 18: Conclusions
Exposome science can overhaul the current environmental health risk assessment paradigm. This requires the combination of:
  Detailed assessment of the state of the environment and human exposure
  high dimensional biology and system science aiming at integration using big data analytics (multi-omics) and bioinformatics
The multi-omics approach focusing on high dimensional biological connectivity permits the identification of molecular paths and biological processes underlying the onset or exacerbation of disease phenotypes associated to exposure to environmental stressors over one’s lifecourse (the exposome)
Precise prevention towards environmental risks by identifying the susceptible or vulnerable individuals or age-groups and cost efficient risk management by identifying the most influential factors
Notes: Exposome science can overhaul the current environmental health risk assessment paradigm. This requires combination of high dimensional biology and system science aiming at integration using big data analytics and bioinformatics
Integrated multi-scale methodology focusing on high dimensional biological connectivity permits the identification of molecular paths and biological processes underlying the onset or exacerbation of disease phenotypes associated to exposure to environmental stressors over one’s lifecourse (the exposome).
The connectivity approach to the exposome elucidates toxicity pathways and assigns causal associations between environmental stressors and health.
Precise prevention by identifying the susceptible or vulnerable individuals or age-groups through analysis of polymorphisms, health medical record and exposure profile (identified by demographic, socioeconomic and habitual parameters)

## Slide 19
Bertold Brecht’s Life of Galileo:
“The main objective of science is not to open the door to infinite wisdom but to roll back the boundaries of infinite error”
Thank you for your attention
www.enve-lab.eu
A connectivity perspective to environmental health